## Slide 1
Subdevice
Without credential burned in the firmware
Gateway Device
Edge
Gateway Device
Edge
Subdevice not registered in the cloud
Sub device registered in the cloud
Add Topology
Device Login
Data Send Telemetries
Calls REST API for dynamic sub device registration and obtains device triple
Edge with device triple burned in the firmware
Subdevice logs in to cloud through edge and presents device triple
Edge burned with SA, edge device productKey, and subdevice productKey
Subdevice logs in to cloud through edge and presents device triple
1.1
1.2
overview_device_connection_2_0_v3_1.png

## Slide 2
Directly Connected Device
With product credentials burned in the firmware
Device Dynamically Activated
Device registered in the cloud
Product has dynamic activation enabled
Device Login
Device Send Telemetries
Device with productKey，
deviceKey, deviceSecret (triple) burned in the firmware
Device registered in the cloud, with device triple burned in the firmware
Present device triple
1. Device activated and presents productKey, productSecret, and DeviceKey
2. Returns deviceSecret
3. Device logs in and presents device triple
Pluggable Acquisition Chip
Device not registered in the cloud
Acquisition chip has SA, productKey burned in firmware
Calls REST API for dynamic device registration and obtains device triple
Presents device triple
2.1
2.2
2.3
overview_device_connection_2_0_v3_2.png

## Slide 3
Inspect
Connection Status
2 - Cloud: Create Product
Create product and obtain ProductKey and ProductSecret
1 - Cloud: Create Model
Define attributes, measure points, services, and events.
3 - Cloud: Create Device
Create device and obtain device triple
Inspect
Connection Status
5 - Device: Connect to Network
Power on device to connect to network. Device carries device triple and request login.
4 - Device: Burn Credentials
Burn device triple into device
6 - Device: Log in
Cloud authenticates device and device logs into cloud. After the first login, device is activated.
7 - Data Transmission
Device starts to send telemetries into cloud.
edge_connection_task_description.png

## Slide 4
Inspect
Connection Status
Obtains ProductKey and ProductSecret
Obtains device triple
Inspect
Connection Status
1 - Cloud: Create Model
（Edge, Subdevice）
Define attributes, measure points, services, and events.
2 - Cloud: Create Product （Edge, Subdevice）
3 - Cloud: Create Device （Edge, Subdevice）
4 - Device: Burn Device Triple（Edge, Subdevice）
Burn device triple into firmware
5 – Edge: Connect to Network
Power on edge to connect to network. Edge carries device triple and request login.
6 – Edge: Log in
Cloud authenticates device and device logs into cloud. After the first login, edge is activated.
7 – Edge: Add Topology
Add subdevices into the topology of the edge gateway
8 – Edge: Proxies Subdevice to Log in
Edge uses the device triple of subdevices and represents subdevices to log in
9 – Data Transmission
Edge, in representative of subdevices, starts to send device telemetries.

## Slide 5
Inspect
Connection Status
云端创建产品网关、子设备
创建产品，获取ProductKey和ProductSecret
云端创建模型网关、子设备
定义设备属性、测点、服务、事件四要素
云端创建网关、子设备实例
在Portal界面创建设备，获得设备三元组
Inspect
Connection Status
网关联网
设备上电联网，携带三元组请求登录云端
实体网关、子设备出厂烧录
烧录三元组
网关登录
云端鉴权，鉴权通过后设备登录，第一次登录即可激活设备
添加拓扑
将子设备添加到网关拓扑下
1
2
3
4
5
6
7
网关代理子设备登录
网关使用子设备三元组代理登录子设备
数据传输
子设备登录后，网关代理子设备发送数据至云端
8
9

## Slide 6
EnOS cloud
App
App
App
App
Edge
MQTT
Edge
Device
registration
service
Device
3rd Party
System
Device
3rd Party
System
Device
3rd Party
System
API gateway
App
App
IoT Hub
Cloud Edge
Clusters
Edge
Edge
Device
registration
service
Proprietary
Protocol
with SN
1
3
2
4

## Slide 7
EnOS IoT Hub
Edge
Inverter
Inverter
Inverter
Inverter

## Slide 8
EnOS IoT Hub
Edge
SCADA
Wind turbine
Wind turbine
Wind turbine
Wind turbine
SCADA

## Slide 9
Direct-Connected Device
Device burned with product credentials
设备动态注册
Product开启动态注册
设备上线
上报数据
云端已经预注册直连设备
上报productkey，devicekey，devicesecret
上报productkey，
devicekey，devicesecret

## Slide 10
Sub Device
Without credential burned
Gateway Device
IoT edge
Gateway Device
Edge logger
Enable dynamic activation for the product that the sub device belongs to
Edge burned with SA
子设备已在平台预注册
Add Topology
Device Login
Device Send Telemetries
网关已提前拿到子设备Product信息
网关已提前拿到子设备
三元组
使用http接口动态注册
子设备
子设备经由网关代理上线，
上线前会添加拓扑结构